## Slide 1: Combustion Process AEN/TSM 220
Combustion Theory
Air/Fuel Ratios
Causes of Emissions
Emission Control

## Slide 2: Combustion Facts
Oxidization process
  Fuel + Oxygen in
  Carbon Dioxide + Water out
Equation:
C?H?O + O2 → CO2 + H2O
C?H?O + O2 + N2 → CO2 + H2O + N2

## Slide 3
C8H18 + O2 + N2 → CO2 + H2O + N2

## Slide 4
C2H6 O + O2 + N2 → CO2 + H2O + N2

## Slide 5: Combustion Process AEN/TSM 220
Combustion Theory
Air/Fuel Ratios
Causes of Emissions
Emission Control

## Slide 6: Air/Fuel Ratio AEN/TSM 220
Stoichiometric
Sometimes we deviate
Fuel chemistry changes A/F
Atomic Weights
  H = 1
  C = 12
  N = 14
  O = 16

## Slide 7
C8H18 + 12.5 O2 + 47 N2 → 8 CO2 + 9 H2O + 47 N2

## Slide 8
C2H6 O + 3 O2 + 11.3 N2 → 2 CO2 + 3 H2O + 11.3 N2

## Slide 9: Combustion Process AEN/TSM 220
Combustion Theory
Air/Fuel Ratios
Causes of Emissions
Emission Control

## Slide 10
C?H? O + O2 + N2 → CO2 + H2O + N2

## Slide 11: Combustion Process AEN/TSM 220
Combustion Theory
Air/Fuel Ratios
Causes of Emissions
Emission Control

## Slide 12: EPA Emission Requirements

## Slide 13: Emission Trade-offs
High Combustion Efficiency
High combustion temperatures
Reduced smoke
More NOx production
Lower Combustion Temperature
Reduce NOx
Lower efficiency
Soot (carbon particulates)

## Slide 14: Mitigation
Engine/vehicle integrated control
  Injection timing
  Multiple injections
  Integration with transmission (load)
Exhaust treatment strategies:
  EGR: Exhaust Gas Recirculation
    DPF: Diesel Particulate Filter
  SCR: Selective Catalytic Reduction

## Slide 15: Exhaust Gas Recirculation
Recirculate some exhaust gas
Lowers combustion T
Reduces NOx
Reduces power and/or efficiency
Soot (carbon) production

## Slide 16: Diesel Particulate Filter
Ceramic wall traps carbon
Periodic regeneration

## Slide 17: Selective Catalytic Reduction
Reduces NOx to N
Uses Diesel Exhaust Fluid (DEF) (Urea 32.5%)
Requires pumps and heaters

## Slide 18: Summary
Where emissions come from
How we fix them
  Improve combustion process
  EGR
  SCR